## Slide 1
Chapter 12: Signal Conversion and Processing

## Slide 2: Objectives
After studying this chapter, students should be able to:
Understand the process and purpose of Analog to Digital signal conversions, versa.
Explain how ADCs and DACs operate.
Explain the basic concepts of a digital signal processor (DSP).
Describe the basic architecture of a DSP.
Chapter 12: Signal Conversion and Processing

## Slide 3: Contents
12.1. Analog-to-Digital Conversion
12.2. Methods of Analog-to-Digital Conversion
12.3. Methods of Digital-to-Analog Conversion
12.4. Digital Signal Processing
12.5. The Digital Signal Processor (DSP)
Chapter 12: Signal Conversion and Processing

## Slide 4: 12.1. Analog-to-Digital Conversion
Sampling and Filtering
Chapter 12: Signal Conversion and Processing
Sampling is the process of taking discrete measurements of an analog signal at regular intervals.
Each sample captures the amplitude of the signal at that instant.
The more samples taken → the more accurate the digital representation of the waveform.

## Slide 5: 12.1. Analog-to-Digital Conversion
The Sampling Theorem To accurately represent an analog signal, the sampling frequency (fₛₐₘₚₗₑ) must be greater than at least twice the highest frequency (fₐ₍ₘₐₓ₎) of the analog signal.
Chapter 12: Signal Conversion and Processing

## Slide 6: 12.1. Analog-to-Digital Conversion
The Need for Filtering Low-pass filters are essential to remove frequency components above the Nyquist frequency.
If high-frequency signals are not filtered, aliasing occurs.
Use an anti-aliasing filter (low-pass) to eliminate unwanted high frequencies before sampling.
Chapter 12: Signal Conversion and Processing

## Slide 7: 12.1. Analog-to-Digital Conversion
Holding the Sampled Value This sample-and-hold operation results in a “stairstep” waveform that approximates the analog input waveform
Chapter 12: Signal Conversion and Processing

## Slide 8: 12.1. Analog-to-Digital Conversion
Analog-to-Digital Conversion Analog-to-digital conversion is the process of converting the output of the sample and hold circuit to a series of binary codes that represent the amplitude of the analog input at each of the sample times.
Chapter 12: Signal Conversion and Processing

## Slide 9: 12.1. Analog-to-Digital Conversion
Quantization The process of converting an analog value to a code is called quantization. During the quantization process, the ADC converts each sampled value of the analog signal to a binary code.
Chapter 12: Signal Conversion and Processing

## Slide 10: 12.1. Analog-to-Digital Conversion
Quantization Increasing the number of quantization bits greatly enhances the fidelity of the reconstructed analog signal.
Chapter 12: Signal Conversion and Processing

## Slide 11: 12.2. Methods of Analog-to-Digital Conversion
A Quick Look at an Operational Amplifier
Chapter 12: Signal Conversion and Processing

## Slide 12: 12.2. Methods of Analog-to-Digital Conversion
Flash (Simultaneous) Analog-to-Digital Converter
Chapter 12: Signal Conversion and Processing

## Slide 13: 12.2. Methods of Analog-to-Digital Conversion
Dual-Slope Analog-to-Digital Converter
Chapter 12: Signal Conversion and Processing

## Slide 14: 12.2. Methods of Analog-to-Digital Conversion
Successive-Approximation Analog-to-Digital Converter
Chapter 12: Signal Conversion and Processing

## Slide 15: 12.2. Methods of Analog-to-Digital Conversion
Successive-Approximation Analog-to-Digital Converter
Chapter 12: Signal Conversion and Processing

## Slide 16: 12.2. Methods of Analog-to-Digital Conversion
Sigma-Delta Analog-to-Digital Converter
Chapter 12: Signal Conversion and Processing

## Slide 17: 12.2. Methods of Analog-to-Digital Conversion
The Sigma-Delta ADC Functional Block Diagram
Chapter 12: Signal Conversion and Processing

## Slide 18: 12.2. Methods of Analog-to-Digital Conversion
Testing Analog-to-Digital Converters
Chapter 12: Signal Conversion and Processing

## Slide 19: 12.2. Methods of Analog-to-Digital Conversion
Analog-to-Digital Conversion Errors In a flash ADC, for example, a failure of one of the op-amp comparators can cause a missing-code error.
Chapter 12: Signal Conversion and Processing

## Slide 20: 12.3. Methods of Digital-to-Analog Conversion
Binary-Weighted-Input Digital-to-Analog Converter
Chapter 12: Signal Conversion and Processing

## Slide 21: 12.3. Methods of Digital-to-Analog Conversion
The R/2R Ladder Digital-to-Analog Converter
Chapter 12: Signal Conversion and Processing

## Slide 22: 12.3. Methods of Digital-to-Analog Conversion
Testing Digital-to-Analog Converters
Chapter 12: Signal Conversion and Processing

## Slide 23: 12.3. Methods of Digital-to-Analog Conversion
Digital-to-Analog Conversion Errors
Chapter 12: Signal Conversion and Processing

## Slide 24: 12.3. Methods of Digital-to-Analog Conversion
The Reconstruction Filter
Chapter 12: Signal Conversion and Processing

## Slide 25: 12.4. Digital Signal Processing
What is DSP? DSP converts analog signals (e.g., sound, video, sensor data) into digital form.
Enables enhancement, filtering, and transformation of signals for various applications.
Chapter 12: Signal Conversion and Processing

## Slide 26: 12.4. Digital Signal Processing
Digital Signal Processing System – Block Diagram DSP is a specialized, high-speed processor used for real-time computational tasks.
The entire system converts analog signals into digital form → processes them → then outputs a high-quality analog signal.
Chapter 12: Signal Conversion and Processing

## Slide 27: 12.5. The Digital Signal Processor (DSP)
DSP in Signal Processing
Chapter 12: Signal Conversion and Processing

## Slide 28: 12.5. The Digital Signal Processor (DSP)
The DSP in a Cellular Telephone
Chapter 12: Signal Conversion and Processing

## Slide 29: 12.5. The Digital Signal Processor (DSP)
Basic DSP Architecture
Chapter 12: Signal Conversion and Processing

## Slide 30: 12.5. The Digital Signal Processor (DSP)
A Specific DSP
Chapter 12: Signal Conversion and Processing

## Slide 31: 12.5. The Digital Signal Processor (DSP)
Pipeline
Chapter 12: Signal Conversion and Processing

## Slide 32: 12.5. The Digital Signal Processor (DSP)
Packaging
Chapter 12: Signal Conversion and Processing

## Slide 33: SUMMARY
1. Sampling & Nyquist Theorem
Sampling converts an analog signal into discrete pulses representing amplitude.
The sampling frequency must be at least twice the highest frequency (Nyquist theorem).
2. ADC & DAC Conversion
ADC converts analog signals to binary codes.
DAC converts digital codes back into analog signals.
3. Digital Signal Processing (DSP)
DSP refers to processing analog signals in digital form, usually in real time, for the purpose of enhancing or modifying the signal.
4. DSP System Architecture
Includes: Anti-aliasing filter, Sample-and-hold circuit, ADC, DSP, DAC, and Reconstruction filter.
5. DSP Architecture Features
DSP is a specialized processor, optimized for speed and real-time data processing.
Typically based on the Harvard architecture (separate program and data memory).
Supports pipeline operation: fetch, decode, and execute stages.
Chapter 12: Signal Conversion and Processing
Chapter 12: Programmable Logic

## Slide 34: MULTIPLE-CHOICE TEST AND PROBLEMS
Complete the true/false questions, multiple-choice questions, and end-of-chapter exercises in the primary textbook.