## Slide 1: Chapter 9: Counters

## Slide 2: Chapter Objectives
After studying this chapter, students should be able to:
Understand finite state machines (FSMs) and various types of counters - including asynchronous, synchronous, binary, and decade counters.
Analyze and design counter circuits - including timing diagrams, integrated circuit (IC) counters, and practical applications.
Determine and modify the modulus of a counter - including the use of cascaded counters to achieve higher modulus values.
Generate and analyze counting sequences - such as up/down counting and designing specific state sequences.
Decode counter states and troubleshoot errors - including the use of logic gates for decoding and methods to eliminate glitches in counter outputs.

## Slide 3: Chapter Outline
9.1. Finite State Machines 9.2. Asynchronous Counters 9.3. Synchronous Counters 9.4. Up/Down Synchronous Counters 9.5. Design of Synchronous Counters 9.6. Cascaded Counters 9.7. Counter Decoding 9.8. Counter Applications 9.9. Logic Symbols with Dependency Notation
Multiple-choice test and Problems

## Slide 4: 9.1. Finite State Machines
General Models of Finite State Machines (FSMs) consist
Moore Machine: Output depends only on the current state (stored in memory).
Mealy Machine: Output depends on both the current state and the current inputs.
Key Differences
In a Moore machine, output changes only when the state changes.
In a Mealy machine, output can change immediately with input, even if the state hasn't changed.

## Slide 5: 9.1. Finite State Machines
Example – Moore Machine Counter
Design Example
Modulus-25 synchronous binary counter. Counts from 0 to 24, resets to 0 on the 25th clock pulse

## Slide 6: 9.1. Finite State Machines
Example of a Mealy Machine
Variable-Modulus Counter:
  Used in a tablet-bottling system with 3 bottle sizes: 25-tablet, 50-tablet, and 100-tablet bottles.
  Requires a state machine with three terminal counts: 25, 50, 100.

## Slide 7: 9.2. Asynchronous Counters
A 2-Bit Asynchronous Binary Counter Structure and Operation
Timing Diagram

## Slide 8: 9.2. Asynchronous Counters
A 3-Bit Asynchronous Binary Counter Structure and Operation
Timing Diagram
Propagation Delay

## Slide 9: 9.2. Asynchronous Counters
Asynchronous Decade Counters & Partial Decoding This technique allows standard binary counters to implement custom counting ranges like 0–9, useful for digital displays and BCD applications.

## Slide 10: 9.3. Synchronous Counters
A 2-Bit Synchronous Binary Counter
Synchronous counters allow faster and more predictable counting compared to asynchronous (ripple) counters, as all flip-flops are triggered by the same clock pulse.

## Slide 11: 9.3. Synchronous Counters
A 3-Bit Synchronous Binary Counter
The 3-bit synchronous counter ensures accurate operation without the propagation delay found in asynchronous counters, making it ideal for efficient and precise digital circuit design.

## Slide 12: 9.3. Synchronous Counters
A 4-Bit Synchronous Binary Counter
The 4-bit synchronous binary counter provides high performance and optimal accuracy in digital circuit design, making it ideal for counting and timing systems.

## Slide 13: 9.3. Synchronous Counters
A 4-Bit Synchronous Decade (BCD) Counter
The synchronous BCD counter operates accurately and quickly, without the propagation delay found in asynchronous counters.
Applications: clocks, decimal digital displays, and counting systems limited to the range 0–9.

## Slide 14: 9.4. Up/Down Synchronous Counters
Up/Down Counter – 3-Bit Binary Counter
An Up/Down counter can count in both increasing and decreasing binary sequences. The counting direction can be reversed at any point in the sequence.

## Slide 15: 9.5. Design of Synchronous Counters
Step 1: State Diagram A state diagram shows the sequence of states a counter or state machine goes through with each clock pulse. It's the first step in designing any state machine or digital counter.

## Slide 16: 9.5. Design of Synchronous Counters
Step 2: Next-State Table The next state is the state that the counter goes to from its present state upon application of a clock pulse.

## Slide 17: 9.5. Design of Synchronous Counters
Step 3: Flip-Flop Transition Table The transition table is an essential tool in the design of synchronous counters, as it helps determine the exact input conditions required to trigger each flip-flop.

## Slide 18: 9.5. Design of Synchronous Counters
Step 4: Karnaugh Maps
Karnaugh maps (K-maps) are used to determine the logic expressions for the J and K inputs of each flip-flop in the counter.

## Slide 19: 9.5. Design of Synchronous Counters
Step 5: Logic Expressions for Flip-Flop Inputs From the Karnaugh maps, you obtain the following expressions for the J and K inputs of each flip-flop:

## Slide 20: 9.5. Design of Synchronous Counters
Step 6: Counter Implementation The final step is to implement the combinational logic from the expressions for the J and K inputs and connect the flip-flops to form the complete 3-bit Gray code counter as shown in Figure 9–29.

## Slide 21: 9.6. Cascaded Counters
Asynchronous Cascading Asynchronous cascading is a simple and effective way to increase counting range, though it introduces cumulative propagation delay.

## Slide 22: 9.6. Cascaded Counters
Synchronous Cascading Achieve higher-modulus operation by cascading synchronous counters using count enable (CTEN) and terminal count (TC) functions.

## Slide 23: 9.6. Cascaded Counters
Cascaded Counters with Truncated Sequences By using synchronous loading, a cascaded counter with a truncated sequence can accurately achieve any desired divide-by modulus

## Slide 24: 9.7. Counter Decoding
State Decoding in a 3-Bit Binary Counter State decoding is useful in applications such as event triggering, pulse generation, or activating outputs at specific count values.

## Slide 25: 9.7. Counter Decoding
Decoding Glitches Glitches can impact circuit performance and must be considered in high-speed or precision digital designs.

## Slide 26: 9.7. Counter Decoding
Cascaded Counters with Truncated Sequences Glitches can impact circuit performance and must be considered in high-speed or precision digital designs.

## Slide 27: 9.8. Counter Applications
A Digital Clock

## Slide 28: 9.8. Counter Applications
Automobile Parking Control

## Slide 29: 9.8. Counter Applications
Parallel-to-Serial Data Conversion (Multiplexing)

## Slide 30: 9.9. Logic Symbols with Dependency Notation
Qualifying Symbol The label “CTR DIV 16” in Figure 9–55(b) identifies the device as a counter (CTR) with sixteen states (DIV 16).

## Slide 31: SUMMARY
Synchronous vs. Asynchronous Counters:
Asynchronous counters: each stage is triggered by the output of the previous stage.
Synchronous counters: all stages are triggered by the same clock pulse → faster operation.
Maximum Modulus:
The maximum number of states is given by:
Maximum modulus = 2n
where n is the number of flip-flops. The actual modulus can be equal to or less than this maximum value.
Cascaded Counters Modulus:
The overall modulus equals the product of the moduli of individual counters.
Chapter 9: Counters

## Slide 32: MULTIPLE-CHOICE TEST AND PROBLEMS
Complete the true/false questions, multiple-choice questions, and end-of-chapter exercises in the primary textbook.